## Slide 1: Getting the most out of OpenDSS with Python
Adam Birchfield
abirchfield@tamu.edu
Advanced Modeling for Distribution Planning Workshop
April 20, 2017
College Station, Texas, USA

## Slide 2: Customizing beyond core OpenDSS
OpenDSS provides a high-performance simulation engine core
The Common Object Model (COM) interface with Python opens up additional applications
  Automated sets of simulations
  Reading and writing other data formats
  Prototyping new control schemes
  Real-time and online integration
  New data visualization
  Interfacing OpenDSS with other tools such as transmission system simulation

## Slide 3: Python compared to other COM clients: Matlab, Excel, Visual C#
Python is a general-purpose scripting language with quick and simple cross-platform development
Free and open-source, unlike Matlab
Challenges in user interface and packaging
Can be slower than compiled languages, such as C#
Python plotting/graphing and other visualization is more complicated, but also more expandable

## Slide 4: Making the connection
Python is freely available, along with extensive documentation https://www.python.org/
Make sure to register the COM server
The Python module win32com.client provides access to the OpenDSS COM module import win32com.client dssObj = win32com.client. Dispatch("OpenDSSEngine.DSS")
The COM module has a variety of interfaces dssText = dssObj.Text dssCircuit = dssObj.ActiveCircuit dssSolution = dssCircuit.Solution dssElem = dssCircuit.ActiveCktElement dssBus = dssCircuit.ActiveBus

## Slide 5: Basic Operations and Control
Any OpenDSS text command can be called dssText.Command = "compile 'Master.dss'"
DSS object data can be accessed and changed dssCircuit.Capacitors.Name = "capname1" state = dssCircuit.Capacitors.States[0] dssCircuit.Capacitors.States = (1,) dssCircuit.SetActiveBus("sub_lsb") puList = dssBus.puVmagAngle
Circuit simulations can be done dssSolution.Solve()
The solution can be called in smaller steps, with customized actions, with details in a separate doc.

## Slide 6: Ideas for Development
Early Binding on COM Interface – documentation available with the details; this will greatly improve the performance and is helpful for complex simulations
Use Microsoft Excel’s VBA object browser to explore the library object structure and functions of the COM server
Building a Python user interface – consider packages Tkinter and Kivy
Numerical Matlab-like computation in Python, consider the package numpy
Visualization – a good, versatile plotting package is Matplotlib